# Installation Instructions for 76233 Connor ADA Shower

### For installation directly on floor joists

- Unit may be installed directly to floor joists with the addition of extra support joist directly under front lip of shower and extra supports near the drain. (see drawing)

- After adding additional supports verify front lip is sitting directly on additional support and nailing flange is touching back wall.

- Using a level, verify unit is plumb. Unit may need to be shimmed on the joists in order to achieve plumb.  It is recommended to use a wedge shaped shim.

- If all the above criteria are met, fasten unit to walls using nail flanges.  Pre-drill holes for screw insertion using a regular twist drill.

- Drain plumbing can be installed and flooring can be laid to edge of shower lip. Shower bottom should be flush with floor upon completion.